Project description: Localization of VHF and UHF signals in a three dimensional space using USRP software defined radios as receivers.

Problem: Proliferation of low cost UAVs cause a lot more potentially unwanted aircraft in certain air spaces. Having the ability to monitor potentially unwanted and potentially hostile drones will prove to be an extremely valuable ability in surveillance and security purposes.

Method of Operation: The methods of tracking will consist of time difference of arrival and relative received signal strength with doppler shift analysis for additional precision for moving targets. Time synchronization of the receivers will be done using GPS signals. Communication between receivers will be done using standard IP over AX.25 amateur packet radio.

Design Goals:
- Receive and analyze RF signals using the USRP 2920
  - USRP 2920 has the capabilities of receiving signals within frequencies of 100Mhz to 2Ghz
  - Ideally, we would like to be able to monitor arbitrary bandwidths within these frequencies
- Determine location of target signal with reasonable accuracy
- Real time tracking of target signal
- Operation with sub-optimally positioned receivers
  - Knowledge of the signal’s frequency and strength may potentially require different placements of receivers to maintain a certain degree of spatial accuracy
  - Man portable size and weight will allow a flexible positioning of receivers